## Slide 1: Data TRANSFER VIA SOUND CSIT 5110 Presentation
Group members :
Marmik MANISH SHAH 20401494
Vladislav RAZNOSCHIKOV 20390944
Aninda Choudhary 20401688

## Slide 2: INTIAL PLAN
Project focuses on transferring data via sound.
Present this technology by making a mobile application.
Encrypting the data into sound and playing it.
Another one will be to receive the sound and to decode it.

## Slide 3: Achieved
Ability to transfer text data thorough sound.
Android application to send data.
Converting text data into sound and transmitting it.
Using a different smartphone to record and decode data.

## Slide 4: How it works – Converting text to sound
Convert text into its corresponding ASCII value.
Modulate specific frequency for different ASCII value.
Send SINE waves according to the frequency.

## Slide 5: HOW it works – converting sound back to data.
Using Fourier Transform to decompose incoming sound to its constituent frequencies.
Comparing frequency with associated ASCII values.
Building the original text from these ASCII values.

## Slide 6: Challenges , Improvement through Iterations
Through trial and error we figured out that data can be successfully transmitted through frequency modulation.
In our first stage we were only able to transfer lower case characters and space.
After achieving that, we thought of transferring all the alphabets inclusive of lowercase and upper case, special characters, etc.
But while doing this, our audio length increased dramatically.

## Slide 7: Demonstration
Step 1 : Recorded video.
Step 2 : Live demonstration.

## Slide 8: Challenges & Limitations
Data can only be successfully transmitted in the form of text.
Data can only be transmitted over extremely short distance.
Increasing the distance increases possibility of error.
Transfer is very slow.
Need a silent environment otherwise sound interferes with data.

## Slide 9: Future IMPROVEMENTS
Add error-correction algorithms like Solomon-Reed.
To correct errors that creep in due to increase in distance , or other factors.
Increase range of transmission to send larger texts.

## Slide 10: Possible real Life applications
Huge possible real life applications of the following.
Personalized Advertisement in Stores.
Transmission of News, anouncements to people on bus stops, other public places.

## Slide 11: Thank YOU